## Slide 1
Tobin Timmons
TEG Clinical Specialist
Haemonetics Corporation
Thrombelastograph® (TEG®) Coagulation Analyzer

## Slide 2: What is TEG®?
A real time analyzer of whole blood for coagulation
Measures the viscoelastic properties of the hemostasis process functionally, the end-result being the hemostatic plug, or clot
The clot has three main systems and five affecting processes...

## Slide 3: Systems Evaluated With TEG
Activation / Aggregation
Physiologic
Pathologic: Primary & Secondary

## Slide 4
Objectives of TEG-Guided Therapy
  To express function and pinpoint dysfunction in the hemostasis system
    Reference the appropriate types and amounts of blood products needed to correct bleeding from this dysfunction
    Allow accurate anticoagulation or antiplatelet interventions to reduce thrombotic complications without inappropriate bleeding

## Slide 5: Objectives of TEG-Guided Therapy (Cont.)
To distinguish between anatomical and coagulopathic bleeding
To distinguish primary from secondary fibrinolysis, including the consumptive phase
To reduce the use of unnecessary blood products and reduce thrombotic complications

## Slide 6
R
= Platelet function
G = Clot Strength
EPL, LY30
K
R = Reaction time to end of thrombin burst
K = fibrin cross-linkage, fibrinogen function
Angle = fibrinogen function
MA = platelet function in mm
G = MA converted to Kdynes/cm2
EPL = Estimated Percent Lysis, clot breakdown
LY30 = Lysis 30 minutes after MA reached

## Slide 7: Hemostasis Monitoring with TEG
PT/INR
PTT
Bleeding
Time
D-dimer
FDP
Platelet Count
Hemostatic
status
Traditional Hemostasis Tests
Do not define the overall process, just provide pieces of the process!

## Slide 8: Normal TEG® Tracing

## Slide 9: Hemodilution/Anticoagulants

## Slide 10: Heparin Effect
Plain cup
5.8 2.2 59.1 0.0 56.2 6.4 *2.0* *0.4* -1.0 55.0
Heparinase cup
Notes: Explain the use of plain and heparinase cup to see heparin effect. ********Changed color of data to match heparinase tracing.

## Slide 11: Combination Hypercoagulability
Notes: Which came first? How can we know for sure?

## Slide 12: Secondary Fibrinolysis, Stage I DIC
Notes: This tracing presents information that can be interpreted with the strongest indication towards stage I DIC. Typically nothing else should cause this tracing (other than mechanical issues).

## Slide 13: Secondary Fibrinolysis, Stage II DIC
Notes: This tracing presents information that could be interpreted as indicating hypcoagulablility throughout with no significant lysis. The information presented could also be interpreted or indicate that it is not Stage II DIC because it could also be things like overanticoagulation or severe factor deficiency.

## Slide 14: Primary Fibrinolysis - TEG® Tracing

## Slide 15: Normal TEG® Analysis
INCLUDES:
Heparin
LMWH
Coumadin
Arixtra®
Pradaxa®
Xarelto®
Factor Deficiency
Fibrinogen Deficiency
Platelet Function
Clot Strength
Lysis
Surgical Bleeding from Hemostasis
Hypercoagulability
EXCLUDES:
Plavix®
Effient®
Brilinta®
Integrilin®
Reopro®
Aggrastat
Pletal((
Persantine
NSAIDs
ASA
Pathologic Platelet Inhibition

## Slide 16: PlateletMapping® Assay
Monitoring Platelet Inhibition and Baseline Platelet Function

## Slide 17: PlateletMapping™ What is it?
Should only be run preop or >12 hours post op
Measures the effect of antiplatelet agents on platelet function
Measures the patient’s maximum platelet function as a reference point
Measures the percentage of inhibition relative to the patient’s reference point
Measures the percentage of inhibition related to other causes: i.e. herbal supplements
Notes: PlateletMapping is a specially-designed assay for the TEG analyzer. It measures the effect of anti-platelet agents on platelet function.
The assay provides two endpoints:
The patient’s maximum platelet function as a reference point
The percentage of inhibition relative to the patient’s reference point
In addition, the PlateletMapping assay identifies resistance or subtherapeutic response to anti-platelet agents, providing clinicians with the information needed to individualize treatment.

## Slide 18: Thrombelastograph Parameters
R (min) - Time to initial fibrin formation induced by thrombin
MA Thrombin - Maximum clot strength induced by thrombin
MA Fibrin - Maximum contribution of fibrin only to MA
MA ADP or A.A - Measures ADP or arachidonic acid stimulated clot strength
R
mm
0
Minutes
Notes: From the tracing we measured multiple TEG parameters:
1. The time from the start of the sample run to the first significant level of fibrin generation is the R time. 2. MA thrombin is a measure of the effect of thrombin- activated platelet aggregation and fibrin mesh formation on total clot strength.
3. Fibrin formation alone is stimulated by reptilase in the presence of heparin.
4. To isolate the platelet contribution to clot strength agonists, either A.A. or ADP are added in the presence of heparin and reptilase
5. The responsiveness to a specific drug is calculated by the above formula. ( pause and point to formula) where Ma thrombin provides maximum clot strength and MA ADP and MA fibrin represent the relative contributions of platelet aggregation and f irbrin formation respectively.
6. Clopidogrel non-responsiveness is defined when the MA ADP exceeds 50% maximum platelet aggregation.

## Slide 20: Temporary Operator – click logon (no password required)

## Slide 21: Filter Patient
Filter patient button

## Slide 22: Highlight Patient Name, Click Done

## Slide 23: Only See Your Patient’s Tracings

## Slide 24: Tracing in Max View

## Slide 25: Normal Tracing Overlay

## Slide 26: Only See Your Patient’s Tracings

## Slide 27: Platelet mapping tracing selection
1
2
3

## Slide 28: Platelet Mapping Overlay – 89% inhibition -Apply % inhibition from preop mapping result to subsequent TEG’s post op

## Slide 29: Sample Draw Instructions
Access: A-line or 21g or larger needle
Blue top tube (citrated 1.8ml) x 2
  If platelet mapping – also need dark Green top (sodium or lithium Heparin – NO GEL). Preop or >12hrs post op.
Waste 1st tube if this is the only blood being drawn
Label:
  patient name
  draw time
  TEG or Platelet Mapping
Sample must be hand delivered to Lab – NO TUBING

## Slide 30: TEG is normal – patient is bleeding
Consider:
  Was there any inhibition demonstrated on the preop platelet mapping?
  vWF deficiency – often ruled out with DDAVP
  Low Ca+ levels (Ca+ is a cofactor in the coagulation cascade)
  Mechanical bleed - reexploration

## Slide 31: Questions?
Thanks for your time!
Tobin Timmons
TEG clinical specialist
850-974-2829